## Slide 1: Completion Object Overview
June 2013
WITSML/PRODML Standards

## Slide 2: Completion Object Project
Started: May, 2011 with participation from both WITSML and PRODML
Participating companies: Chevron (sponsoring operator), Weatherford, Peloton, (lead vendors), Schlumberger, Paradigm, ExxonMobil, BP, Total, Halliburton with Energistics
Delivery for Special Interest Group and subsequent public review: January 2013.
After review, final version release: June 2013

## Slide 3
Business Case and Benefits

## Slide 4: High Level Application of Completion Object
Drilling – Production hand-offs
  DB to DB sync & transfer
  Initial completion & subsequent workovers
Initial Completion transfer from rig
Well services through life of asset
Engineering applications transfers
  Eg, Nodal analysis models
  Well surveillance
Primary Initial Usage

## Slide 5: Primary Initial Use Case: Over the Well Lifecycle, Drilling & Production MUST Pass Data Back and Forth
Drilled
Well
New Completion
Drilling & Completions Domain
Production Domain
Workover Planned
As Completed
Well
Perm.
Gauge
DTS
Tubing
Perforations
SSSV
Packer
Completion DB
Drilling system
WITSML
Drilling Data
Completion Data
Well Services
Data Updates
Current
Now Enabled
E.g. Gas Lift
Change
Primary Initial Usage

## Slide 6: Business Drivers and Benefits
Eliminate multiple data entry requirements thereby improving accuracy and saving time
Improved safety. Knowledge of what is down hole will improve operations
Improved data consistency, accuracy, quality
Improved planning and scheduling (through faster access to better quality data and by eliminating manual re-entry of data)
Reduce reliance on paper or spread sheet well files

## Slide 7
Concepts for Completion Object

## Slide 8: Three Use Cases dealt with in this release
Snapshot of completion at a point in time
  “what is current status?” eg for completion diagram, engineering application eg Nodal
Change Log of events which alter completion between one time and another
  Eg, from well services contractor
Cumulative History – whole life of well capable of generating current snapshot or any previous one
  Eg, for sync or transfer between databases

## Slide 9
Perm.
Gauge
DTS
Tubing
Perforations
SSSV
Packer
Casing
Example Snapshot at One Instant
Snapshot is akin to a completion diagram at one instant in time

## Slide 10: Example Change Log for Single Job
Perm.
Gauge
DTS
Tubing
Perforations
SSSV
Packer
Casing
Perm.
Gauge
DTS
Tubing
SSSV
Packer
Casing
Perforation Job
Perforations
Well CM [Construction and Maintenance] Ledger entry
Data concerning change, in Downhole Components

## Slide 11: Example Well Cumulative History
Day 1
Day 4
Events
Well equipment
Well CM Ledger gets added to cumulatively
Downhole Components added, updated or removed by Events

## Slide 12: Data Organization
4 top-level objects:
Downhole Component - contains wellbore equipment
Well Construction Management Ledger - contains details of Jobs & Events
Well Completion –associates a wellhead stream with one or more wellbore completions (completed zones) in the well
Wellbore Completion – represents a section of wellbore open to flow with reservoir.

## Slide 13: Scope of Downhole Components
Wellhead: not described in full detail
Borehole: the open hole sizes as drilled
Casings: multiple strings supported, can include joint tally
Cement: placement as well as properties (also other fills)
Tubings: multiple strings supported, can include joint tally
Accessories to strings: e.g. packers, gas lift valves
Perforation Set: physical description of perforations etc.
Formation Layers: with basic properties
Wellhead
Downhole String Set
Perforation Sets
Accessory
Borehole String Set
Assembly: groups of components
Equipment: the components used
String Equipment

## Slide 14: Scope of Well Construction Management Ledger
Identity information such as the well name
Event Information, eg depth & time ranges of operation
Completion reference information including references to string, equipment.
Operational/management information eg, business associate, w/order number, cost, rig ID, flags if operation was planned/unplanned etc.
eventExtension - contains the job data (limited types), may have reference to details in a WITSML object
Participant – enables link to be made to any WITSML object, eg a log. No semantic meaning conveyed.

## Slide 15: Nesting of Jobs containing multiple Events
An event in the ledger can have a parent event ID.
Events can be organized into a hierarchy.
Eg, “Job Producer” = top level event
  “Sub Job” Events with this “Job Producer” parent:
  “Job – Well Service Rig Crew”
  “Job – Site Work”
  “Job – Tubing Inspection”
  From Different Service providers
  Hence, each service provider can supply their report to operator using the data-object

## Slide 16: Scope of Flow Paths, Reservoir to Wellhead
Well Completion: a commingled “flow” in the well, eg “X”
Not Specified: flow through specific tubing strings etc
String Equipment: has
Ref’d Perforated Intervals: from this component (eg casing)
References Perf set, borehole, equipment as appropriate
AND Geology feature
Wellbore Completion: section of borehole open to flow , eg “A”
Contact Interval: physical connection to reservoir,
4 types: perf, o/h, slot, g/p
A References Well Completion X
Contains Contact Intervals
These would be further Wellbore Completions & Contact Intervals, linked to the 2nd tubing string’s Well Completion
Perforation Set: physical perforation details
Parent =well
Parent =wellbore
Parent = downholeComponent

## Slide 17: Role of Well and Wellbore in Completion
The whole completion spans multiple wellbores so Downhole Components has parent Well
Well Completion (where Well “flows” are defined has parent Well
Borehole has parent downhole component and is associated with a wellbore
String and Equipment have parent downhole component and are associated with a wellbore (the end (bottom) point will define which wellbore)
Wellbore Completion and Contact Interval has parent wellbore
Each wellCMLedger entry in wellCMLedgers can apply to a different well (in addition to wellbore)

## Slide 18: Future Plans (Possible)
Surveillance, flow paths etc – where are instruments, flows reported & measured (PDGs, DTS, etc.)
  in complex completions especially
Optimization – addition of inflow performance and description, fluid properties  Nodal Analysis
Reservoir connection made explicit e.g. with link to RESQML layers
Tree and surface equipment
Further “xxxJob” objects, eg perfJob, gravelPackJob, which contain full details of operations (not just “end result” of the jobs)

## Slide 19: Other (secondary) Use Cases in Production Domain
Perm.
Gauge
DTS
Flowing
Intervals, sensor depths
Surveillance/
Reporting
Optimization
Optimization using Nodal models
Production Domain
Completion DB

## Slide 20: Summary
A Major new Capability for life of well completion data management
Needs promotion and adoption now
Potential to Expand Data Coverage and Usage
Potential to support new “Well Services DOF” industry approach with standard services reporting method